CM 5 Lambda 470 MHz
CE
SY WL=0.638	'Wave Length
SY L=5
SY angle1=23.955	'18.85 degrees at start
SY angle2=angle1	'26.1 degrees at start
SY FG=0.0095	'Feed Gap / 2
SY TR=470	'Termination Resistance
SY AGL=0	'Height Above Ground
GW	1	1	0	FG	AGL	0	-FG	AGL	#12
GW	2	125	0	FG	AGL	cos(angle1)*L*WL	FG+(sin(angle1)*L*WL)	AGL	#12
GW	3	125	cos(angle1)*L*WL	FG+(sin(angle1)*L*WL)	AGL	(cos(angle1)*L*WL)+(cos(angle2)*L*WL)	FG+(sin(angle1)*L*WL)-(sin(angle2)*L*WL)	AGL	#12
GW	4	125	0	-FG	AGL	cos(angle2)*L*WL	-FG-(sin(angle2)*L*WL)	AGL	#12
GW	5	125	cos(angle2)*L*WL	-FG-(sin(angle2)*L*WL)	AGL	(cos(angle2)*L*WL)+(cos(angle1)*L*WL)	-FG-(sin(angle2)*L*WL)+(sin(angle1)*L*WL)	AGL	#12
GW	6	1	(cos(angle1)*L*WL)+(cos(angle2)*L*WL)	FG+(sin(angle1)*L*WL)-(sin(angle2)*L*WL)	AGL	(cos(angle1)*L*WL)+(cos(angle2)*L*WL)	-FG-(sin(angle2)*L*WL)+(sin(angle1)*L*WL)	AGL	#12
GW	100	1	-WL/4	FG	AGL+0.0014	-WL/4	-FG	AGL+0.0014	#12
GE	0
EK
EX	0	100	1	0	1	0	0
LD	0	6	1	1	TR	0	0
LD	5	0	0	0	58000000
GN	-1
TL	100	1	1	1	300	0	0	0	0	0
' FR 0 0 0 0 470 0	' Fixed Freq
' FR 0 29 0 0 470 12	' Freq Sweep 470-806 every 12 MHz - OLD UHF BAND
' FR 0 34 0 0 410 12	' Freq Sweep 410-806 every 12 MHz - Even Wider Sweep
FR 0 39 0 0 470 6	' Freq Sweep 470-698 every 6 MHz - PREFERRED FOR UHF
' FR 0 77 0 0 470 3	' Freq Sweep 470-698 every 3 MHz
' FR 0 153 0 0 470 1.5	' Freq Sweep 470-698 every 1.5 MHz
' FR 0 71 0 0 300 10	' Freq Sweep 300-1000 every 10 MHz - WIDEBAND SWEEP
' FR Hi-VHF choices:
' FR 0 15 0 0 174 3	' Freq Sweep 174-216 every 3 MHz
' FR 0 29 0 0 174 1.5	' Freq Sweep 174-216 every 1.5 MHz - PREFERRED
' FR 0 45 0 0 162 1.5	' Freq Sweep 162-228 every 1.5 MHz - Add +/- 12 MHz BW
' FR 0 27 0 0 189 1.5	' Freq Sweep 186-228 every 1.5 MHz - SPECIAL
' FR 0 43 0 0 174 1	' Freq Sweep 174-216 every 1 MHz - Hi-Rez
' FR 0 23 0 0 198 1	' Freq Sweep 198-220 every 1 MHz - Hi-Rez - Ch13 SPECIAL
' FR 0 26 0 0 150 6	' Freq Sweep 150-300 every 6 MHz - WIDEBAND SWEEP
' FR Lo-VHF choices:
' FR 0 19 0 0 54 3	' Frequency Sweep every 3 MHz for Ch2-6 + FM
' FR 0 35 0 0 54 1	' Frequency Sweep every 1 MHz for Ch2-6
' FR 0 36 0 0 75 1	' Frequency Sweep every 1 MHz for Ch5 + Ch6 + FM
' FR 0 28 0 0 54 6	' Wide Freq Sweep every 6 MHz for Ch2-13
' FR 0 64 0 0 54 12	' Super Wide Freq Sweep 54-810 every 12 MHz
' RP choices in order of increasing calculation time:
' RP 0 1 1 1510 90 90 1 1 0 0	' 1D Gain toward 0-deg Azimuth - SIDE GAIN
' RP 0 1 1 1510 90 0 1 1 0 0	' 1D Gain toward 90-deg Azimuth - FORWARD GAIN
' RP 0 1 1 1510 90 180 1 1 0 0	' 1D Gain toward 270-deg Azimuth - REVERSE GAIN
' RP 0 1 37 1510 90 0 1 5 0 0	' 2D (Left only) Azimuthal Gain Slice
' RP 0 1 73 1510 90 0 1 5 0 0	' 2D Azimuthal Gain Slice - PREFERRED
' RP 0 73 1 1510 90 0 5 1 0 0	' 2D Elevation Gain Slice
' RP 0 73 73 1510 90 0 5 5 0 0	' 3D Lower Hemisphere reveals antenna (Fixed Freq)
' RP 0 285 73 1510 90 0 5 5 0 0	' 3D Full Coverage obscures antenna (Fixed Freq)
RP 0 1 146 1510 90 0 1 2.5 0 0
EN